## Slide 1
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter 25 — Translation Hardware
GRADUATE LECTURE
• Virtual memory would be unnecessarily expensive if every load required a full uncached traversal of page tables.
• Translation hardware therefore caches recently useful mappings.
• This cache is related to, but distinct from, the caches that hold instruction and data bytes.
• A program can have excellent data-cache behavior and still suffer from poor translation locality. [ R3 , R10 ]
CHAPTER 25 | 1
Notes: SLIDE 1: Chapter 25 — Translation Hardware
LECTURE NARRATION
Virtual memory would be unnecessarily expensive if every load required a full uncached traversal of page tables. Translation hardware therefore caches recently useful mappings. This cache is related to, but distinct from, the caches that hold instruction and data bytes. A program can have excellent data-cache behavior and still suffer from poor translation locality. [ R3 , R10 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, virtual memory would be unnecessarily expensive if every load required a full uncached traversal of page tables.

## Slide 2
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
What This Chapter Builds
LEARNING OBJECTIVES
• Explain the mechanisms and contracts in Translation Hardware.
• Trace the chapter's important state, representation, and resource transitions.
• Identify failure modes, assumptions, and evidence required for correctness.
• Apply the chapter model to the worked examples and guided lab.
CHAPTER 25 | 2
Notes: SLIDE 2: What This Chapter Builds
LECTURE NARRATION
Virtual memory would be unnecessarily expensive if every load required a full uncached traversal of page tables. Translation hardware therefore caches recently useful mappings. This cache is related to, but distinct from, the caches that hold instruction and data bytes. A program can have excellent data-cache behavior and still suffer from poor translation locality. [ R3 , R10 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, virtual memory would be unnecessarily expensive if every load required a full uncached traversal of page tables.

## Slide 3
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter Roadmap
SOURCE-ALIGNED COVERAGE
• 25.1 MMU
• 25.2 TLB
• 25.3 TLB hits
• 25.4 TLB misses
• ...plus 5 additional source topics
CHAPTER 25 | 3
Notes: SLIDE 3: Chapter Roadmap
LECTURE NARRATION
25.1 MMU 25.2 TLB 25.3 TLB hits 25.4 TLB misses ...plus 5 additional source topics
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, 25.1 MMU 25.2 TLB 25.3 TLB hits 25.4 TLB misses ...plus 5 additional source topics

## Slide 4
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.1 MMU
SOURCE TOPIC
• The memory-management unit, or MMU, is the processor machinery involved in translation and access checking.
• It interprets the configured address-space structures according to architectural rules.
• Its implementation can include several translation caches and page-walk optimizations.
• The MMU does not understand a source-level vector or ownership model.
CHAPTER 25 | 4
Notes: SLIDE 4: 25.1 MMU
LECTURE NARRATION
The memory-management unit, or MMU, is the processor machinery involved in translation and access checking. It interprets the configured address-space structures according to architectural rules. Its implementation can include several translation caches and page-walk optimizations. The MMU does not understand a source-level vector or ownership model. It knows translation and permission information at the architecture’s supported granularity. This explains why a legal machine address can still produce undefined behavior in C or C++: the language may forbid an access that hardware page checks permit.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the memory-management unit, or MMU, is the processor machinery involved in translation and access checking.

## Slide 5
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.1 MMU — Deep Dive
ENGINEERING IMPLICATIONS
• The MMU does not understand a source-level vector or ownership model.
• It knows translation and permission information at the architecture’s supported granularity.
• This explains why a legal machine address can still produce undefined behavior in C or C++: the language may forbid an access that hardware page checks permit.
CHAPTER 25 | 5
Notes: SLIDE 5: 25.1 MMU — Deep Dive
LECTURE NARRATION
The memory-management unit, or MMU, is the processor machinery involved in translation and access checking. It interprets the configured address-space structures according to architectural rules. Its implementation can include several translation caches and page-walk optimizations. The MMU does not understand a source-level vector or ownership model. It knows translation and permission information at the architecture’s supported granularity. This explains why a legal machine address can still produce undefined behavior in C or C++: the language may forbid an access that hardware page checks permit.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the memory-management unit, or MMU, is the processor machinery involved in translation and access checking.

## Slide 6
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.2 TLB
SOURCE TOPIC
• A translation lookaside buffer, or TLB, caches translations and associated permission information.
• A matching entry can supply the physical-frame relationship without a complete new walk.
• Real processors may have distinct instruction and data TLBs, multiple levels, and different handling for page sizes.
• TLB entries must be interpreted in the correct address-space context.
CHAPTER 25 | 6
Notes: SLIDE 6: 25.2 TLB
LECTURE NARRATION
A translation lookaside buffer, or TLB, caches translations and associated permission information. A matching entry can supply the physical-frame relationship without a complete new walk. Real processors may have distinct instruction and data TLBs, multiple levels, and different handling for page sizes. TLB entries must be interpreted in the correct address-space context. Hardware and kernels can use address-space identifiers and other mechanisms to retain useful entries across switches without confusing one process’s mapping with another’s. Do not assume either that every switch flushes every translation or that retaining entries requires no context tagging.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a translation lookaside buffer, or TLB, caches translations and associated permission information.

## Slide 7
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.2 TLB — Deep Dive
ENGINEERING IMPLICATIONS
• TLB entries must be interpreted in the correct address-space context.
• Hardware and kernels can use address-space identifiers and other mechanisms to retain useful entries across switches without confusing one process’s mapping with another’s.
• Do not assume either that every switch flushes every translation or that retaining entries requires no context tagging.
CHAPTER 25 | 7
Notes: SLIDE 7: 25.2 TLB — Deep Dive
LECTURE NARRATION
A translation lookaside buffer, or TLB, caches translations and associated permission information. A matching entry can supply the physical-frame relationship without a complete new walk. Real processors may have distinct instruction and data TLBs, multiple levels, and different handling for page sizes. TLB entries must be interpreted in the correct address-space context. Hardware and kernels can use address-space identifiers and other mechanisms to retain useful entries across switches without confusing one process’s mapping with another’s. Do not assume either that every switch flushes every translation or that retaining entries requires no context tagging.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a translation lookaside buffer, or TLB, caches translations and associated permission information.

## Slide 8
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.3 TLB hits
SOURCE TOPIC
• A TLB hit occurs when a usable cached translation matches the access.
• The processor can then proceed with the relevant permission checks and physical-address use.
• This is a translation hit, not necessarily a data-cache hit.
• The translated data may still be absent from L1, L2, or the last-level cache.
CHAPTER 25 | 8
Notes: SLIDE 8: 25.3 TLB hits
LECTURE NARRATION
A TLB hit occurs when a usable cached translation matches the access. The processor can then proceed with the relevant permission checks and physical-address use. This is a translation hit, not necessarily a data-cache hit. The translated data may still be absent from L1, L2, or the last-level cache. Conversely, the bytes may already exist in a data cache while translation requires additional work. A complete access model therefore tracks translation and data access as related but separate paths.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a TLB hit occurs when a usable cached translation matches the access.

## Slide 9
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.3 TLB hits — Deep Dive
ENGINEERING IMPLICATIONS
• The translated data may still be absent from L1, L2, or the last-level cache.
• Conversely, the bytes may already exist in a data cache while translation requires additional work.
• A complete access model therefore tracks translation and data access as related but separate paths.
CHAPTER 25 | 9
Notes: SLIDE 9: 25.3 TLB hits — Deep Dive
LECTURE NARRATION
A TLB hit occurs when a usable cached translation matches the access. The processor can then proceed with the relevant permission checks and physical-address use. This is a translation hit, not necessarily a data-cache hit. The translated data may still be absent from L1, L2, or the last-level cache. Conversely, the bytes may already exist in a data cache while translation requires additional work. A complete access model therefore tracks translation and data access as related but separate paths.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a TLB hit occurs when a usable cached translation matches the access.

## Slide 10
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.4 TLB misses
SOURCE TOPIC
• A TLB miss means that the required translation is not available in the consulted translation cache.
• The processor can search another translation level or perform a page-table walk.
• If the tables describe a valid permitted mapping, the translation can be installed and the access can continue without a page fault.
• A page fault occurs when translation or protection rules cannot complete the access as requested.
CHAPTER 25 | 10
Notes: SLIDE 10: 25.4 TLB misses
LECTURE NARRATION
A TLB miss means that the required translation is not available in the consulted translation cache. The processor can search another translation level or perform a page-table walk. If the tables describe a valid permitted mapping, the translation can be installed and the access can continue without a page fault. A page fault occurs when translation or protection rules cannot complete the access as requested. It requires software handling on the reference system. The distinction is essential: TLB miss does not imply page fault , and neither event is synonymous with a data-cache miss.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a TLB miss means that the required translation is not available in the consulted translation cache.

## Slide 11
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.4 TLB misses — Deep Dive
ENGINEERING IMPLICATIONS
• A page fault occurs when translation or protection rules cannot complete the access as requested.
• It requires software handling on the reference system.
• The distinction is essential: TLB miss does not imply page fault , and neither event is synonymous with a data-cache miss.
CHAPTER 25 | 11
Notes: SLIDE 11: 25.4 TLB misses — Deep Dive
LECTURE NARRATION
A TLB miss means that the required translation is not available in the consulted translation cache. The processor can search another translation level or perform a page-table walk. If the tables describe a valid permitted mapping, the translation can be installed and the access can continue without a page fault. A page fault occurs when translation or protection rules cannot complete the access as requested. It requires software handling on the reference system. The distinction is essential: TLB miss does not imply page fault , and neither event is synonymous with a data-cache miss.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a TLB miss means that the required translation is not available in the consulted translation cache.

## Slide 12
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.5 Translation caching
SOURCE TOPIC
• Translation caching rewards locality in the set of pages accessed.
• A rough measure called TLB reach multiplies the number of usable entries by the page size, but associativity, separate structures, mixed page sizes, and access patterns can...
• For a teaching cache with 64 entries and 4-KiB pages, nominal reach is 256 KiB.
• A loop touching one byte in each of 1024 different pages can have a small useful-byte working set but a large translation working set.
CHAPTER 25 | 12
Notes: SLIDE 12: 25.5 Translation caching
LECTURE NARRATION
Translation caching rewards locality in the set of pages accessed. A rough measure called TLB reach multiplies the number of usable entries by the page size, but associativity, separate structures, mixed page sizes, and access patterns can reduce the usefulness of that simple estimate. For a teaching cache with 64 entries and 4-KiB pages, nominal reach is 256 KiB. A loop touching one byte in each of 1024 different pages can have a small useful-byte working set but a large translation working set. Packing those bytes into fewer pages can improve translation locality without changing the number of logical items.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, translation caching rewards locality in the set of pages accessed.

## Slide 13
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
25.5 Translation caching — Deep Dive
ENGINEERING IMPLICATIONS
• For a teaching cache with 64 entries and 4-KiB pages, nominal reach is 256 KiB.
• A loop touching one byte in each of 1024 different pages can have a small useful-byte working set but a large translation working set.
• Packing those bytes into fewer pages can improve translation locality without changing the number of logical items.
CHAPTER 25 | 13
Notes: SLIDE 13: 25.5 Translation caching — Deep Dive
LECTURE NARRATION
Translation caching rewards locality in the set of pages accessed. A rough measure called TLB reach multiplies the number of usable entries by the page size, but associativity, separate structures, mixed page sizes, and access patterns can reduce the usefulness of that simple estimate. For a teaching cache with 64 entries and 4-KiB pages, nominal reach is 256 KiB. A loop touching one byte in each of 1024 different pages can have a small useful-byte working set but a large translation working set. Packing those bytes into fewer pages can improve translation locality without changing the number of logical items.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, translation caching rewards locality in the set of pages accessed.

## Slide 14
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Translation and data are separate events
SOURCE TOPIC
• Assume a fully associative, four-entry LRU TLB and a repeating virtual-page trace:
• The first four accesses miss and install translations.
• The next four hit, giving 4 hits in 8 accesses, or 50% over the entire cold trace.
• Repeating the four-page cycle afterward yields hits while no other activity evicts entries.
CHAPTER 25 | 14
Notes: SLIDE 14: Worked example — Translation and data are separate events
LECTURE NARRATION
Assume a fully associative, four-entry LRU TLB and a repeating virtual-page trace: The first four accesses miss and install translations. The next four hit, giving 4 hits in 8 accesses, or 50% over the entire cold trace. Repeating the four-page cycle afterward yields hits while no other activity evicts entries. Now use five pages: Every access misses under this particular capacity and replacement model. By the time a page is reused, the other four pages have displaced it. This trace does not establish anything about whether the data bytes are in L1 or DRAM, and it does not require any page fault when all mappings remain valid. An experiment that touches one byte per page should distinguish cold page allocation, first-touch faults, TLB behavior, and data-cache behavior. Timing the first traversal alone mixes several effects. A useful design initializes the mapping, records the access pattern, repeats controlled passes, and uses available counters only when their meaning and permissions are understood.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, assume a fully associative, four-entry LRU TLB and a repeating virtual-page trace: The first four accesses miss and install translations.

## Slide 15
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Translation and data are separate events — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• The first four accesses miss and install translations.
• The next four hit, giving 4 hits in 8 accesses, or 50% over the entire cold trace.
• Repeating the four-page cycle afterward yields hits while no other activity evicts entries.
• Now use five pages:
CHAPTER 25 | 15
Notes: SLIDE 15: Worked example — Translation and data are separate events — Deep Dive
LECTURE NARRATION
Assume a fully associative, four-entry LRU TLB and a repeating virtual-page trace: The first four accesses miss and install translations. The next four hit, giving 4 hits in 8 accesses, or 50% over the entire cold trace. Repeating the four-page cycle afterward yields hits while no other activity evicts entries. Now use five pages: Every access misses under this particular capacity and replacement model. By the time a page is reused, the other four pages have displaced it. This trace does not establish anything about whether the data bytes are in L1 or DRAM, and it does not require any page fault when all mappings remain valid. An experiment that touches one byte per page should distinguish cold page allocation, first-touch faults, TLB behavior, and data-cache behavior. Timing the first traversal alone mixes several effects. A useful design initializes the mapping, records the access pattern, repeats controlled passes, and uses available counters only when their meaning and permissions are understood.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, assume a fully associative, four-entry LRU TLB and a repeating virtual-page trace: The first four accesses miss and install translations.

## Slide 16
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — TLB speedup intuition
SOURCE TOPIC
• Without a TLB, a multilevel page-table walk can require several memory references before the actual data access.
• On a TLB hit, the cached translation supplies the frame mapping immediately, avoiding those walk references.
• The data cache lookup is still a separate concern; a TLB hit does not imply the requested data is in L1.
CHAPTER 25 | 16
Notes: SLIDE 16: Worked example — TLB speedup intuition
LECTURE NARRATION
Without a TLB, a multilevel page-table walk can require several memory references before the actual data access. On a TLB hit, the cached translation supplies the frame mapping immediately, avoiding those walk references. The data cache lookup is still a separate concern; a TLB hit does not imply the requested data is in L1.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, without a TLB, a multilevel page-table walk can require several memory references before the actual data access.

## Slide 17
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — TLB speedup intuition — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• Without a TLB, a multilevel page-table walk can require several memory references before the actual data access.
• On a TLB hit, the cached translation supplies the frame mapping immediately, avoiding those walk references.
• The data cache lookup is still a separate concern; a TLB hit does not imply the requested data is in L1.
CHAPTER 25 | 17
Notes: SLIDE 17: Worked example — TLB speedup intuition — Deep Dive
LECTURE NARRATION
Without a TLB, a multilevel page-table walk can require several memory references before the actual data access. On a TLB hit, the cached translation supplies the frame mapping immediately, avoiding those walk references. The data cache lookup is still a separate concern; a TLB hit does not imply the requested data is in L1.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, without a TLB, a multilevel page-table walk can require several memory references before the actual data access.

## Slide 18
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Handling a TLB miss
SOURCE TOPIC
• On a hardware-managed design, a TLB miss triggers a page-table walk.
• If the required PTEs are valid, the translation is inserted into the TLB and the memory access proceeds.
• If the walk discovers an absent or disallowed mapping, the result becomes a page fault rather than a successful TLB fill.
CHAPTER 25 | 18
Notes: SLIDE 18: Worked example — Handling a TLB miss
LECTURE NARRATION
On a hardware-managed design, a TLB miss triggers a page-table walk. If the required PTEs are valid, the translation is inserted into the TLB and the memory access proceeds. If the walk discovers an absent or disallowed mapping, the result becomes a page fault rather than a successful TLB fill.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, on a hardware-managed design, a TLB miss triggers a page-table walk.

## Slide 19
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Handling a TLB miss — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• On a hardware-managed design, a TLB miss triggers a page-table walk.
• If the required PTEs are valid, the translation is inserted into the TLB and the memory access proceeds.
• If the walk discovers an absent or disallowed mapping, the result becomes a page fault rather than a successful TLB fill.
CHAPTER 25 | 19
Notes: SLIDE 19: Worked example — Handling a TLB miss — Deep Dive
LECTURE NARRATION
On a hardware-managed design, a TLB miss triggers a page-table walk. If the required PTEs are valid, the translation is inserted into the TLB and the memory access proceeds. If the walk discovers an absent or disallowed mapping, the result becomes a page fault rather than a successful TLB fill.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, on a hardware-managed design, a TLB miss triggers a page-table walk.

## Slide 20
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Guided lab and review
SOURCE TOPIC
• Lab 25.
• Simulate the two traces using a list ordered from least recently used to most recently used.
• Add hit and miss counters.
• Repeat with five entries and explain which results change.
CHAPTER 25 | 20
Notes: SLIDE 20: Guided lab and review
LECTURE NARRATION
Lab 25. Simulate the two traces using a list ordered from least recently used to most recently used. Add hit and miss counters. Repeat with five entries and explain which results change. Review 1. Can a TLB hit be followed by a data-cache miss? Review 2. Why can large strides increase translation pressure?
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, lab 25.

## Slide 21
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Guided lab and review — Deep Dive
LAB, REVIEW & ACCEPTANCE
• Review 1.
• Can a TLB hit be followed by a data-cache miss?
• Review 2.
• Why can large strides increase translation pressure?
CHAPTER 25 | 21
Notes: SLIDE 21: Guided lab and review — Deep Dive
LECTURE NARRATION
Lab 25. Simulate the two traces using a list ordered from least recently used to most recently used. Add hit and miss counters. Repeat with five entries and explain which results change. Review 1. Can a TLB hit be followed by a data-cache miss? Review 2. Why can large strides increase translation pressure?
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, lab 25.

## Slide 22
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter Synthesis
KEY TAKEAWAYS
• The chapter's central subject is translation hardware.
• Correct reasoning requires explicit assumptions, bounds, ownership, and interface contracts.
• Observed behavior is evidence about a run; it is not automatically a language or system guarantee.
• Use the worked examples and lab to test whether the model transfers to new cases.
CHAPTER 25 | 22
Notes: SLIDE 22: Chapter Synthesis
LECTURE NARRATION
The chapter's central subject is translation hardware. Correct reasoning requires explicit assumptions, bounds, ownership, and interface contracts. Observed behavior is evidence about a run; it is not automatically a language or system guarantee. Use the worked examples and lab to test whether the model transfers to new cases.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the chapter's central subject is translation hardware.

## Slide 23
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Review and Transition
CHECK YOUR MODEL
• Explain one mechanism from the chapter without relying on vocabulary alone.
• Identify one failure mode and the violated contract or invariant.
• State what evidence would support your diagnosis and what it would not prove.
• Next: Page Faults.
CHAPTER 25 | 23
Notes: SLIDE 23: Review and Transition
LECTURE NARRATION
Explain one mechanism from the chapter without relying on vocabulary alone. Identify one failure mode and the violated contract or invariant. State what evidence would support your diagnosis and what it would not prove. Next: Page Faults.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, explain one mechanism from the chapter without relying on vocabulary alone.