## Slide 1
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter 24 — Page Tables
GRADUATE LECTURE
• A page table describes mappings and their permissions.
• Large address spaces make a single fully populated flat table expensive, so many architectures use a hierarchy in which intermediate entries point to lower-level tables.
• Unused regions can then avoid allocating all possible lower-level structures. [ R3 , R10 ]
CHAPTER 24 | 1
Notes: SLIDE 1: Chapter 24 — Page Tables
LECTURE NARRATION
A page table describes mappings and their permissions. Large address spaces make a single fully populated flat table expensive, so many architectures use a hierarchy in which intermediate entries point to lower-level tables. Unused regions can then avoid allocating all possible lower-level structures. [ R3 , R10 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a page table describes mappings and their permissions.

## Slide 2
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
What This Chapter Builds
LEARNING OBJECTIVES
• Explain the mechanisms and contracts in Page Tables.
• Trace the chapter's important state, representation, and resource transitions.
• Identify failure modes, assumptions, and evidence required for correctness.
• Apply the chapter model to the worked examples and guided lab.
CHAPTER 24 | 2
Notes: SLIDE 2: What This Chapter Builds
LECTURE NARRATION
A page table describes mappings and their permissions. Large address spaces make a single fully populated flat table expensive, so many architectures use a hierarchy in which intermediate entries point to lower-level tables. Unused regions can then avoid allocating all possible lower-level structures. [ R3 , R10 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a page table describes mappings and their permissions.

## Slide 3
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter Roadmap
SOURCE-ALIGNED COVERAGE
• 24.1 Page-table entries
• 24.2 Present bit
• 24.3 Writable bit
• 24.4 User-accessible bit
• ...plus 7 additional source topics
CHAPTER 24 | 3
Notes: SLIDE 3: Chapter Roadmap
LECTURE NARRATION
24.1 Page-table entries 24.2 Present bit 24.3 Writable bit 24.4 User-accessible bit ...plus 7 additional source topics
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, 24.1 Page-table entries 24.2 Present bit 24.3 Writable bit 24.4 User-accessible bit ...plus 7 additional source topics

## Slide 4
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.1 Page-table entries
SOURCE TOPIC
• A page-table entry encodes mapping information and control bits.
• Depending on its level and configuration, it can point to another table or describe a mapped page.
• It may include a physical address, presence information, access permissions, and status used by memory-management policy.
• An entry is not a portable C structure whose bit layout can be guessed from a diagram for another architecture.
CHAPTER 24 | 4
Notes: SLIDE 4: 24.1 Page-table entries
LECTURE NARRATION
A page-table entry encodes mapping information and control bits. Depending on its level and configuration, it can point to another table or describe a mapped page. It may include a physical address, presence information, access permissions, and status used by memory-management policy. An entry is not a portable C structure whose bit layout can be guessed from a diagram for another architecture. Kernel code must follow the architecture’s encoding and required update procedures. Ordinary user programs should reason about the behavior exposed by mapping APIs instead of attempting to manipulate active page tables.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
The program uses a map of memory addresses. The operating system translates that map to where the data is actually stored.

## Slide 5
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.1 Page-table entries — Deep Dive
ENGINEERING IMPLICATIONS
• An entry is not a portable C structure whose bit layout can be guessed from a diagram for another architecture.
• Kernel code must follow the architecture’s encoding and required update procedures.
• Ordinary user programs should reason about the behavior exposed by mapping APIs instead of attempting to manipulate active page tables.
CHAPTER 24 | 5
Notes: SLIDE 5: 24.1 Page-table entries — Deep Dive
LECTURE NARRATION
A page-table entry encodes mapping information and control bits. Depending on its level and configuration, it can point to another table or describe a mapped page. It may include a physical address, presence information, access permissions, and status used by memory-management policy. An entry is not a portable C structure whose bit layout can be guessed from a diagram for another architecture. Kernel code must follow the architecture’s encoding and required update procedures. Ordinary user programs should reason about the behavior exposed by mapping APIs instead of attempting to manipulate active page tables.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
The program uses a map of memory addresses. The operating system translates that map to where the data is actually stored.

## Slide 6
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.2 Present bit
SOURCE TOPIC
• A present indicator tells hardware whether an entry is valid for the corresponding translation step.
• An absent entry can cause a page fault.
• The kernel may use nonpresent encodings and its own metadata to remember whether the region is demand-paged, swapped, invalid, or associated with another policy.
• Therefore, “not present” does not automatically mean “read this page from disk.” The handler must first establish that the access is legitimate.
CHAPTER 24 | 6
Notes: SLIDE 6: 24.2 Present bit
LECTURE NARRATION
A present indicator tells hardware whether an entry is valid for the corresponding translation step. An absent entry can cause a page fault. The kernel may use nonpresent encodings and its own metadata to remember whether the region is demand-paged, swapped, invalid, or associated with another policy. Therefore, “not present” does not automatically mean “read this page from disk.” The handler must first establish that the access is legitimate. A zero-filled anonymous page may require no file read at all. A completely invalid address must not be repaired by granting access merely because a fault occurred.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a present indicator tells hardware whether an entry is valid for the corresponding translation step.

## Slide 7
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.2 Present bit — Deep Dive
ENGINEERING IMPLICATIONS
• Therefore, “not present” does not automatically mean “read this page from disk.” The handler must first establish that the access is legitimate.
• A zero-filled anonymous page may require no file read at all.
• A completely invalid address must not be repaired by granting access merely because a fault occurred.
CHAPTER 24 | 7
Notes: SLIDE 7: 24.2 Present bit — Deep Dive
LECTURE NARRATION
A present indicator tells hardware whether an entry is valid for the corresponding translation step. An absent entry can cause a page fault. The kernel may use nonpresent encodings and its own metadata to remember whether the region is demand-paged, swapped, invalid, or associated with another policy. Therefore, “not present” does not automatically mean “read this page from disk.” The handler must first establish that the access is legitimate. A zero-filled anonymous page may require no file read at all. A completely invalid address must not be repaired by granting access merely because a fault occurred.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a present indicator tells hardware whether an entry is valid for the corresponding translation step.

## Slide 8
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.3 Writable bit
SOURCE TOPIC
• A writable permission controls whether stores are allowed under the architecture’s access rules.
• A mapping can be readable without being writable.
• Copy-on-write commonly uses a temporarily nonwritable hardware mapping for a region that is logically permitted to become privately writable after a fault.
• Permission interpretation can involve multiple levels and processor controls.
CHAPTER 24 | 8
Notes: SLIDE 8: 24.3 Writable bit
LECTURE NARRATION
A writable permission controls whether stores are allowed under the architecture’s access rules. A mapping can be readable without being writable. Copy-on-write commonly uses a temporarily nonwritable hardware mapping for a region that is logically permitted to become privately writable after a fault. Permission interpretation can involve multiple levels and processor controls. It is unsafe to inspect only one leaf bit and conclude that an access must succeed. The complete translation and protection state determines the result. This chapter’s exercises state a simplified combined-permission rule explicitly.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a writable permission controls whether stores are allowed under the architecture’s access rules.

## Slide 9
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.3 Writable bit — Deep Dive
ENGINEERING IMPLICATIONS
• Permission interpretation can involve multiple levels and processor controls.
• It is unsafe to inspect only one leaf bit and conclude that an access must succeed.
• The complete translation and protection state determines the result.
• This chapter’s exercises state a simplified combined-permission rule explicitly.
CHAPTER 24 | 9
Notes: SLIDE 9: 24.3 Writable bit — Deep Dive
LECTURE NARRATION
A writable permission controls whether stores are allowed under the architecture’s access rules. A mapping can be readable without being writable. Copy-on-write commonly uses a temporarily nonwritable hardware mapping for a region that is logically permitted to become privately writable after a fault. Permission interpretation can involve multiple levels and processor controls. It is unsafe to inspect only one leaf bit and conclude that an access must succeed. The complete translation and protection state determines the result. This chapter’s exercises state a simplified combined-permission rule explicitly.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a writable permission controls whether stores are allowed under the architecture’s access rules.

## Slide 10
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.4 User-accessible bit
SOURCE TOPIC
• A user/supervisor permission distinguishes mappings accessible to user-mode code from mappings reserved for privileged access.
• It helps prevent an application from treating kernel data as ordinary user memory even when some related address range exists in the broader translation structure.
• This hardware distinction does not replace file permissions, process credentials, or application authorization.
• A user-accessible buffer may still contain data that an application should not disclose to a particular network client.
CHAPTER 24 | 10
Notes: SLIDE 10: 24.4 User-accessible bit
LECTURE NARRATION
A user/supervisor permission distinguishes mappings accessible to user-mode code from mappings reserved for privileged access. It helps prevent an application from treating kernel data as ordinary user memory even when some related address range exists in the broader translation structure. This hardware distinction does not replace file permissions, process credentials, or application authorization. A user-accessible buffer may still contain data that an application should not disclose to a particular network client. Memory-access enforcement and application-level information policy operate at different layers.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a user/supervisor permission distinguishes mappings accessible to user-mode code from mappings reserved for privileged access.

## Slide 11
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.4 User-accessible bit — Deep Dive
ENGINEERING IMPLICATIONS
• This hardware distinction does not replace file permissions, process credentials, or application authorization.
• A user-accessible buffer may still contain data that an application should not disclose to a particular network client.
• Memory-access enforcement and application-level information policy operate at different layers.
CHAPTER 24 | 11
Notes: SLIDE 11: 24.4 User-accessible bit — Deep Dive
LECTURE NARRATION
A user/supervisor permission distinguishes mappings accessible to user-mode code from mappings reserved for privileged access. It helps prevent an application from treating kernel data as ordinary user memory even when some related address range exists in the broader translation structure. This hardware distinction does not replace file permissions, process credentials, or application authorization. A user-accessible buffer may still contain data that an application should not disclose to a particular network client. Memory-access enforcement and application-level information policy operate at different layers.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a user/supervisor permission distinguishes mappings accessible to user-mode code from mappings reserved for privileged access.

## Slide 12
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.5 Multilevel page tables
SOURCE TOPIC
• A multilevel design divides the virtual page number into several indexes.
• Each index selects an entry in the current table; that entry leads to the next level until a mapping is found.
• Large-page entries can terminate a walk earlier when the architecture supports them.
• A familiar x86-64 example uses four levels with 9 index bits per level and a 12-bit offset, describing a 48-bit virtual-address organization subject to canonical-address rules.
CHAPTER 24 | 12
Notes: SLIDE 12: 24.5 Multilevel page tables
LECTURE NARRATION
A multilevel design divides the virtual page number into several indexes. Each index selects an entry in the current table; that entry leads to the next level until a mapping is found. Large-page entries can terminate a walk earlier when the architecture supports them. A familiar x86-64 example uses four levels with 9 index bits per level and a 12-bit offset, describing a 48-bit virtual-address organization subject to canonical-address rules. Other configurations can add a fifth level and expand the address width. The exact layout is a platform fact, not a consequence of the C++ pointer type alone. [ R3 , R10 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
The program uses a map of memory addresses. The operating system translates that map to where the data is actually stored.

## Slide 13
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.5 Multilevel page tables — Deep Dive
ENGINEERING IMPLICATIONS
• A familiar x86-64 example uses four levels with 9 index bits per level and a 12-bit offset, describing a 48-bit virtual-address organization subject to canonical-address...
• Other configurations can add a fifth level and expand the address width.
• The exact layout is a platform fact, not a consequence of the C++ pointer type alone. [ R3 , R10 ]
CHAPTER 24 | 13
Notes: SLIDE 13: 24.5 Multilevel page tables — Deep Dive
LECTURE NARRATION
A multilevel design divides the virtual page number into several indexes. Each index selects an entry in the current table; that entry leads to the next level until a mapping is found. Large-page entries can terminate a walk earlier when the architecture supports them. A familiar x86-64 example uses four levels with 9 index bits per level and a 12-bit offset, describing a 48-bit virtual-address organization subject to canonical-address rules. Other configurations can add a fifth level and expand the address width. The exact layout is a platform fact, not a consequence of the C++ pointer type alone. [ R3 , R10 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
The program uses a map of memory addresses. The operating system translates that map to where the data is actually stored.

## Slide 14
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.6 Page-table walks
SOURCE TOPIC
• A page-table walk follows the hierarchy to resolve a translation.
• Hardware performs walks on the reference architecture, potentially using internal caches for table information.
• The naive count of one ordinary memory access per level is a useful upper-level teaching model but not a complete performance prediction.
• A walk can stop because it finds a valid leaf mapping, encounters an absent entry, or detects a protection problem.
CHAPTER 24 | 14
Notes: SLIDE 14: 24.6 Page-table walks
LECTURE NARRATION
A page-table walk follows the hierarchy to resolve a translation. Hardware performs walks on the reference architecture, potentially using internal caches for table information. The naive count of one ordinary memory access per level is a useful upper-level teaching model but not a complete performance prediction. A walk can stop because it finds a valid leaf mapping, encounters an absent entry, or detects a protection problem. Once a translation is cached in a TLB, later accesses can avoid repeating the full walk until the entry is evicted or invalidated. The next chapter separates translation caching from data caching.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
The program uses a map of memory addresses. The operating system translates that map to where the data is actually stored.

## Slide 15
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.6 Page-table walks — Deep Dive
ENGINEERING IMPLICATIONS
• A walk can stop because it finds a valid leaf mapping, encounters an absent entry, or detects a protection problem.
• Once a translation is cached in a TLB, later accesses can avoid repeating the full walk until the entry is evicted or invalidated.
• The next chapter separates translation caching from data caching.
CHAPTER 24 | 15
Notes: SLIDE 15: 24.6 Page-table walks — Deep Dive
LECTURE NARRATION
A page-table walk follows the hierarchy to resolve a translation. Hardware performs walks on the reference architecture, potentially using internal caches for table information. The naive count of one ordinary memory access per level is a useful upper-level teaching model but not a complete performance prediction. A walk can stop because it finds a valid leaf mapping, encounters an absent entry, or detects a protection problem. Once a translation is cached in a TLB, later accesses can avoid repeating the full walk until the entry is evicted or invalidated. The next chapter separates translation caching from data caching.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
The program uses a map of memory addresses. The operating system translates that map to where the data is actually stored.

## Slide 16
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.7 Memory protection
SOURCE TOPIC
• Protection checks combine the requested operation with the applicable mapping permissions and architectural state.
• Reading data, writing data, and fetching instructions are not necessarily governed by identical permissions.
• Non-executable mappings help separate data storage from executable code.
• Changing a page-table entry is not enough when processors retain cached translations based on the old state.
CHAPTER 24 | 16
Notes: SLIDE 16: 24.7 Memory protection
LECTURE NARRATION
Protection checks combine the requested operation with the applicable mapping permissions and architectural state. Reading data, writing data, and fetching instructions are not necessarily governed by identical permissions. Non-executable mappings help separate data storage from executable code. Changing a page-table entry is not enough when processors retain cached translations based on the old state. The system must perform the required invalidation and coordination. On a multicore system, other cores may also hold relevant translations; this is the reason for translation invalidation mechanisms often discussed as TLB shootdowns.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, protection checks combine the requested operation with the applicable mapping permissions and architectural state.

## Slide 17
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
24.7 Memory protection — Deep Dive
ENGINEERING IMPLICATIONS
• Changing a page-table entry is not enough when processors retain cached translations based on the old state.
• The system must perform the required invalidation and coordination.
• On a multicore system, other cores may also hold relevant translations; this is the reason for translation invalidation mechanisms often discussed as TLB shootdowns.
CHAPTER 24 | 17
Notes: SLIDE 17: 24.7 Memory protection — Deep Dive
LECTURE NARRATION
Protection checks combine the requested operation with the applicable mapping permissions and architectural state. Reading data, writing data, and fetching instructions are not necessarily governed by identical permissions. Non-executable mappings help separate data storage from executable code. Changing a page-table entry is not enough when processors retain cached translations based on the old state. The system must perform the required invalidation and coordination. On a multicore system, other cores may also hold relevant translations; this is the reason for translation invalidation mechanisms often discussed as TLB shootdowns.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, protection checks combine the requested operation with the applicable mapping permissions and architectural state.

## Slide 18
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — A two-level address decomposition
SOURCE TOPIC
• Use a 16-bit teaching address space with 256-byte pages and two levels of 16-entry tables.
• The address fields are:
• Address 0xABCD yields outer index 0xA , inner index 0xB , and offset 0xCD .
• Suppose outer entry A points to a valid inner table and inner entry B maps frame 0x34 .
CHAPTER 24 | 18
Notes: SLIDE 18: Worked example — A two-level address decomposition
LECTURE NARRATION
Use a 16-bit teaching address space with 256-byte pages and two levels of 16-entry tables. The address fields are: Address 0xABCD yields outer index 0xA , inner index 0xB , and offset 0xCD . Suppose outer entry A points to a valid inner table and inner entry B maps frame 0x34 . The translated address is 0x34CD in a physical model that supports that frame number. Now add permissions. The outer entry allows user reads and writes, but the inner entry allows only user reads. A user load succeeds; a user store fails. For this model, effective permissions are the intersection of the permissions along the path. Giving the outer entry more authority cannot override a restrictive leaf entry. A flat table for all 256 virtual pages needs 256 entries. The two-level arrangement needs one 16-entry outer table plus 16 entries for each allocated inner table. With only one populated inner table, it uses 32 entries; with all 16 inner tables allocated, it uses 272 entries. Hierarchy saves space for sparse mappings but is not automatically smaller for a fully populated tiny address space.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
Think of an address written on a note: the note can tell you where to look, but it does not prove the thing is still there or that you are allowed to use it.

## Slide 19
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — A two-level address decomposition — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• Address 0xABCD yields outer index 0xA , inner index 0xB , and offset 0xCD .
• Suppose outer entry A points to a valid inner table and inner entry B maps frame 0x34 .
• The translated address is 0x34CD in a physical model that supports that frame number.
• Now add permissions.
CHAPTER 24 | 19
Notes: SLIDE 19: Worked example — A two-level address decomposition — Deep Dive
LECTURE NARRATION
Use a 16-bit teaching address space with 256-byte pages and two levels of 16-entry tables. The address fields are: Address 0xABCD yields outer index 0xA , inner index 0xB , and offset 0xCD . Suppose outer entry A points to a valid inner table and inner entry B maps frame 0x34 . The translated address is 0x34CD in a physical model that supports that frame number. Now add permissions. The outer entry allows user reads and writes, but the inner entry allows only user reads. A user load succeeds; a user store fails. For this model, effective permissions are the intersection of the permissions along the path. Giving the outer entry more authority cannot override a restrictive leaf entry. A flat table for all 256 virtual pages needs 256 entries. The two-level arrangement needs one 16-entry outer table plus 16 entries for each allocated inner table. With only one populated inner table, it uses 32 entries; with all 16 inner tables allocated, it uses 272 entries. Hierarchy saves space for sparse mappings but is not automatically smaller for a fully populated tiny address space.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
Think of an address written on a note: the note can tell you where to look, but it does not prove the thing is still there or that you are allowed to use it.

## Slide 20
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Walking a two-level table
SOURCE TOPIC
• Suppose a simplified address uses 10 bits for level-1 index, 10 for level-2 index, and 12 offset bits.
• The hardware extracts the top index to locate a level-2 table, then uses the second index to locate the final PTE.
• If the present and permission bits allow the access, the physical frame number from the PTE is concatenated with the original 12-bit offset.
CHAPTER 24 | 20
Notes: SLIDE 20: Worked example — Walking a two-level table
LECTURE NARRATION
Suppose a simplified address uses 10 bits for level-1 index, 10 for level-2 index, and 12 offset bits. The hardware extracts the top index to locate a level-2 table, then uses the second index to locate the final PTE. If the present and permission bits allow the access, the physical frame number from the PTE is concatenated with the original 12-bit offset.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, suppose a simplified address uses 10 bits for level-1 index, 10 for level-2 index, and 12 offset bits.

## Slide 21
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Walking a two-level table — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• Suppose a simplified address uses 10 bits for level-1 index, 10 for level-2 index, and 12 offset bits.
• The hardware extracts the top index to locate a level-2 table, then uses the second index to locate the final PTE.
• If the present and permission bits allow the access, the physical frame number from the PTE is concatenated with the original 12-bit offset.
CHAPTER 24 | 21
Notes: SLIDE 21: Worked example — Walking a two-level table — Deep Dive
LECTURE NARRATION
Suppose a simplified address uses 10 bits for level-1 index, 10 for level-2 index, and 12 offset bits. The hardware extracts the top index to locate a level-2 table, then uses the second index to locate the final PTE. If the present and permission bits allow the access, the physical frame number from the PTE is concatenated with the original 12-bit offset.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, suppose a simplified address uses 10 bits for level-1 index, 10 for level-2 index, and 12 offset bits.

## Slide 22
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Permission check on a write
SOURCE TOPIC
• A valid PTE can still reject an access.
• If the page is present and user-accessible but its writable bit is clear, a user-mode store raises a protection fault.
• A load from the same page may succeed.
• Presence and permission are separate dimensions of the mapping.
CHAPTER 24 | 22
Notes: SLIDE 22: Worked example — Permission check on a write
LECTURE NARRATION
A valid PTE can still reject an access. If the page is present and user-accessible but its writable bit is clear, a user-mode store raises a protection fault. A load from the same page may succeed. Presence and permission are separate dimensions of the mapping.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a valid PTE can still reject an access.

## Slide 23
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Permission check on a write — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• A valid PTE can still reject an access.
• If the page is present and user-accessible but its writable bit is clear, a user-mode store raises a protection fault.
• A load from the same page may succeed.
• Presence and permission are separate dimensions of the mapping.
CHAPTER 24 | 23
Notes: SLIDE 23: Worked example — Permission check on a write — Deep Dive
LECTURE NARRATION
A valid PTE can still reject an access. If the page is present and user-accessible but its writable bit is clear, a user-mode store raises a protection fault. A load from the same page may succeed. Presence and permission are separate dimensions of the mapping.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a valid PTE can still reject an access.

## Slide 24
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Guided lab and review
SOURCE TOPIC
• Lab 24.
• Translate 0x27F0 in the teaching model when outer entry 2 selects a table whose entry 7 maps frame 0x19 .
• Calculate table-entry storage for three allocated inner tables.
• Review 1.
CHAPTER 24 | 24
Notes: SLIDE 24: Guided lab and review
LECTURE NARRATION
Lab 24. Translate 0x27F0 in the teaching model when outer entry 2 selects a table whose entry 7 maps frame 0x19 . Calculate table-entry storage for three allocated inner tables. Review 1. Why can a permission change require work on other cores? Review 2. Does an absent entry identify the backing-storage policy by itself?
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, lab 24.

## Slide 25
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Guided lab and review — Deep Dive
LAB, REVIEW & ACCEPTANCE
• Review 1.
• Why can a permission change require work on other cores?
• Review 2.
• Does an absent entry identify the backing-storage policy by itself?
CHAPTER 24 | 25
Notes: SLIDE 25: Guided lab and review — Deep Dive
LECTURE NARRATION
Lab 24. Translate 0x27F0 in the teaching model when outer entry 2 selects a table whose entry 7 maps frame 0x19 . Calculate table-entry storage for three allocated inner tables. Review 1. Why can a permission change require work on other cores? Review 2. Does an absent entry identify the backing-storage policy by itself?
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, lab 24.

## Slide 26
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter Synthesis
KEY TAKEAWAYS
• The chapter's central subject is page tables.
• Correct reasoning requires explicit assumptions, bounds, ownership, and interface contracts.
• Observed behavior is evidence about a run; it is not automatically a language or system guarantee.
• Use the worked examples and lab to test whether the model transfers to new cases.
CHAPTER 24 | 26
Notes: SLIDE 26: Chapter Synthesis
LECTURE NARRATION
The chapter's central subject is page tables. Correct reasoning requires explicit assumptions, bounds, ownership, and interface contracts. Observed behavior is evidence about a run; it is not automatically a language or system guarantee. Use the worked examples and lab to test whether the model transfers to new cases.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the chapter's central subject is page tables.

## Slide 27
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Review and Transition
CHECK YOUR MODEL
• Explain one mechanism from the chapter without relying on vocabulary alone.
• Identify one failure mode and the violated contract or invariant.
• State what evidence would support your diagnosis and what it would not prove.
• Next: Translation Hardware.
CHAPTER 24 | 27
Notes: SLIDE 27: Review and Transition
LECTURE NARRATION
Explain one mechanism from the chapter without relying on vocabulary alone. Identify one failure mode and the violated contract or invariant. State what evidence would support your diagnosis and what it would not prove. Next: Translation Hardware.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, explain one mechanism from the chapter without relying on vocabulary alone.