## Slide 1
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter 12 — Instruction Set Architecture
GRADUATE LECTURE
• The instruction set is the boundary between software’s requested operations and a processor’s implementation.
• It describes registers, instructions, address calculations, and architectural effects.
• It does not specify that every instruction takes one cycle or that internal work occurs in source order.
• Reading assembly well requires keeping the architectural result separate from the microarchitectural method.
CHAPTER 12 | 1
Notes: SLIDE 1: Chapter 12 — Instruction Set Architecture
LECTURE NARRATION
The instruction set is the boundary between software’s requested operations and a processor’s implementation. It describes registers, instructions, address calculations, and architectural effects. It does not specify that every instruction takes one cycle or that internal work occurs in source order. Reading assembly well requires keeping the architectural result separate from the microarchitectural method.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the instruction set is the boundary between software’s requested operations and a processor’s implementation.

## Slide 2
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
What This Chapter Builds
LEARNING OBJECTIVES
• Explain the mechanisms and contracts in Instruction Set Architecture.
• Trace the chapter's important state, representation, and resource transitions.
• Identify failure modes, assumptions, and evidence required for correctness.
• Apply the chapter model to the worked examples and guided lab.
CHAPTER 12 | 2
Notes: SLIDE 2: What This Chapter Builds
LECTURE NARRATION
The instruction set is the boundary between software’s requested operations and a processor’s implementation. It describes registers, instructions, address calculations, and architectural effects. It does not specify that every instruction takes one cycle or that internal work occurs in source order. Reading assembly well requires keeping the architectural result separate from the microarchitectural method.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the instruction set is the boundary between software’s requested operations and a processor’s implementation.

## Slide 3
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter Roadmap
SOURCE-ALIGNED COVERAGE
• 12.1 Machine instructions
• 12.2 Registers
• 12.3 Memory
• 12.4 Program counter
• ...plus 6 additional source topics
CHAPTER 12 | 3
Notes: SLIDE 3: Chapter Roadmap
LECTURE NARRATION
12.1 Machine instructions 12.2 Registers 12.3 Memory 12.4 Program counter ...plus 6 additional source topics
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, 12.1 Machine instructions 12.2 Registers 12.3 Memory 12.4 Program counter ...plus 6 additional source topics

## Slide 4
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.1 Machine instructions
SOURCE TOPIC
• A machine instruction is an encoded operation the processor recognizes.
• It identifies an operation and, explicitly or implicitly, its operands.
• Instructions can move data, perform arithmetic, change control flow, or request privileged behavior.
• On x86-64, instructions have variable-length encodings rather than one fixed size.
CHAPTER 12 | 4
Notes: SLIDE 4: 12.1 Machine instructions
LECTURE NARRATION
A machine instruction is an encoded operation the processor recognizes. It identifies an operation and, explicitly or implicitly, its operands. Instructions can move data, perform arithmetic, change control flow, or request privileged behavior. On x86-64, instructions have variable-length encodings rather than one fixed size. The visible instruction sequence is not necessarily the processor’s internal execution sequence. A processor may decode instructions into smaller operations, overlap independent work, and speculate past branches. Architectural rules determine what results may become visible. An assembly listing is therefore a semantic description and an input to performance analysis, not a cycle-by-cycle hardware trace.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a machine instruction is an encoded operation the processor recognizes.

## Slide 5
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.1 Machine instructions — Deep Dive
ENGINEERING IMPLICATIONS
• The visible instruction sequence is not necessarily the processor’s internal execution sequence.
• A processor may decode instructions into smaller operations, overlap independent work, and speculate past branches.
• Architectural rules determine what results may become visible.
• An assembly listing is therefore a semantic description and an input to performance analysis, not a cycle-by-cycle hardware trace.
CHAPTER 12 | 5
Notes: SLIDE 5: 12.1 Machine instructions — Deep Dive
LECTURE NARRATION
A machine instruction is an encoded operation the processor recognizes. It identifies an operation and, explicitly or implicitly, its operands. Instructions can move data, perform arithmetic, change control flow, or request privileged behavior. On x86-64, instructions have variable-length encodings rather than one fixed size. The visible instruction sequence is not necessarily the processor’s internal execution sequence. A processor may decode instructions into smaller operations, overlap independent work, and speculate past branches. Architectural rules determine what results may become visible. An assembly listing is therefore a semantic description and an input to performance analysis, not a cycle-by-cycle hardware trace.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a machine instruction is an encoded operation the processor recognizes.

## Slide 6
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.2 Registers
SOURCE TOPIC
• Registers are named architectural storage locations used directly by instructions.
• General-purpose registers hold integer values and addresses.
• Other register classes support vector, floating-point, control, and status operations.
• Keeping a value in a register can avoid a memory access, but the number and use of registers are constrained by the ISA and ABI.
CHAPTER 12 | 6
Notes: SLIDE 6: 12.2 Registers
LECTURE NARRATION
Registers are named architectural storage locations used directly by instructions. General-purpose registers hold integer values and addresses. Other register classes support vector, floating-point, control, and status operations. Keeping a value in a register can avoid a memory access, but the number and use of registers are constrained by the ISA and ABI. Architectural register names need not correspond one-to-one with fixed physical storage inside a modern processor. Register renaming can map successive architectural values to different physical registers. This helps remove false dependencies while preserving the program’s required register behavior. Source-level programmers normally need the architectural model first and the renaming model only for deeper performance work.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, registers are named architectural storage locations used directly by instructions.

## Slide 7
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.2 Registers — Deep Dive
ENGINEERING IMPLICATIONS
• Architectural register names need not correspond one-to-one with fixed physical storage inside a modern processor.
• Register renaming can map successive architectural values to different physical registers.
• This helps remove false dependencies while preserving the program’s required register behavior.
• Source-level programmers normally need the architectural model first and the renaming model only for deeper performance work.
CHAPTER 12 | 7
Notes: SLIDE 7: 12.2 Registers — Deep Dive
LECTURE NARRATION
Registers are named architectural storage locations used directly by instructions. General-purpose registers hold integer values and addresses. Other register classes support vector, floating-point, control, and status operations. Keeping a value in a register can avoid a memory access, but the number and use of registers are constrained by the ISA and ABI. Architectural register names need not correspond one-to-one with fixed physical storage inside a modern processor. Register renaming can map successive architectural values to different physical registers. This helps remove false dependencies while preserving the program’s required register behavior. Source-level programmers normally need the architectural model first and the renaming model only for deeper performance work.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, registers are named architectural storage locations used directly by instructions.

## Slide 8
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.3 Memory
SOURCE TOPIC
• Instructions access memory through effective addresses computed from available operands.
• A load brings a value into a register or another destination; a store writes a value to memory.
• Some x86 instructions combine memory access with arithmetic, but that does not eliminate the underlying data movement.
• A memory operand can involve address translation, cache lookup, coherence, and fault checks.
CHAPTER 12 | 8
Notes: SLIDE 8: 12.3 Memory
LECTURE NARRATION
Instructions access memory through effective addresses computed from available operands. A load brings a value into a register or another destination; a store writes a value to memory. Some x86 instructions combine memory access with arithmetic, but that does not eliminate the underlying data movement. A memory operand can involve address translation, cache lookup, coherence, and fault checks. Two instructions with similar arithmetic can have very different costs if one waits for a cache miss. Count memory traffic and dependencies, not just mnemonics, when estimating performance.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, instructions access memory through effective addresses computed from available operands.

## Slide 9
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.3 Memory — Deep Dive
ENGINEERING IMPLICATIONS
• A memory operand can involve address translation, cache lookup, coherence, and fault checks.
• Two instructions with similar arithmetic can have very different costs if one waits for a cache miss.
• Count memory traffic and dependencies, not just mnemonics, when estimating performance.
CHAPTER 12 | 9
Notes: SLIDE 9: 12.3 Memory — Deep Dive
LECTURE NARRATION
Instructions access memory through effective addresses computed from available operands. A load brings a value into a register or another destination; a store writes a value to memory. Some x86 instructions combine memory access with arithmetic, but that does not eliminate the underlying data movement. A memory operand can involve address translation, cache lookup, coherence, and fault checks. Two instructions with similar arithmetic can have very different costs if one waits for a cache miss. Count memory traffic and dependencies, not just mnemonics, when estimating performance.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, instructions access memory through effective addresses computed from available operands.

## Slide 10
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.4 Program counter
SOURCE TOPIC
• The program counter identifies the instruction position used for control flow.
• On x86-64 the architectural instruction pointer is %rip .
• Sequential execution advances to the next instruction; branches, calls, returns, and exceptions change the flow according to their rules.
• For RIP-relative addressing, the displacement is interpreted relative to the next instruction’s address.
CHAPTER 12 | 10
Notes: SLIDE 10: 12.4 Program counter
LECTURE NARRATION
The program counter identifies the instruction position used for control flow. On x86-64 the architectural instruction pointer is %rip . Sequential execution advances to the next instruction; branches, calls, returns, and exceptions change the flow according to their rules. For RIP-relative addressing, the displacement is interpreted relative to the next instruction’s address. This detail matters when manually calculating a target from disassembly. The value displayed beside an instruction is usually its own starting address, not necessarily the base used in that instruction’s relative-address computation.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the program counter identifies the instruction position used for control flow.

## Slide 11
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.4 Program counter — Deep Dive
ENGINEERING IMPLICATIONS
• For RIP-relative addressing, the displacement is interpreted relative to the next instruction’s address.
• This detail matters when manually calculating a target from disassembly.
• The value displayed beside an instruction is usually its own starting address, not necessarily the base used in that instruction’s relative-address computation.
CHAPTER 12 | 11
Notes: SLIDE 11: 12.4 Program counter — Deep Dive
LECTURE NARRATION
The program counter identifies the instruction position used for control flow. On x86-64 the architectural instruction pointer is %rip . Sequential execution advances to the next instruction; branches, calls, returns, and exceptions change the flow according to their rules. For RIP-relative addressing, the displacement is interpreted relative to the next instruction’s address. This detail matters when manually calculating a target from disassembly. The value displayed beside an instruction is usually its own starting address, not necessarily the base used in that instruction’s relative-address computation.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the program counter identifies the instruction position used for control flow.

## Slide 12
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.5 Processor state
SOURCE TOPIC
• Processor state includes more than general-purpose registers.
• It can include condition flags, vector registers, floating-point control state, stack state, privilege state, and address-translation configuration.
• The exact state relevant to an operation depends on the architecture and execution context.
• A context switch must preserve enough state for a thread to resume as though its execution had been paused.
CHAPTER 12 | 12
Notes: SLIDE 12: 12.5 Processor state
LECTURE NARRATION
Processor state includes more than general-purpose registers. It can include condition flags, vector registers, floating-point control state, stack state, privilege state, and address-translation configuration. The exact state relevant to an operation depends on the architecture and execution context. A context switch must preserve enough state for a thread to resume as though its execution had been paused. A normal function call has a narrower contract: the calling convention specifies which registers the caller or callee must preserve. Confusing a context switch with a function call leads to incorrect assumptions about who saves what.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, processor state includes more than general-purpose registers.

## Slide 13
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.5 Processor state — Deep Dive
ENGINEERING IMPLICATIONS
• A context switch must preserve enough state for a thread to resume as though its execution had been paused.
• A normal function call has a narrower contract: the calling convention specifies which registers the caller or callee must preserve.
• Confusing a context switch with a function call leads to incorrect assumptions about who saves what.
CHAPTER 12 | 13
Notes: SLIDE 13: 12.5 Processor state — Deep Dive
LECTURE NARRATION
Processor state includes more than general-purpose registers. It can include condition flags, vector registers, floating-point control state, stack state, privilege state, and address-translation configuration. The exact state relevant to an operation depends on the architecture and execution context. A context switch must preserve enough state for a thread to resume as though its execution had been paused. A normal function call has a narrower contract: the calling convention specifies which registers the caller or callee must preserve. Confusing a context switch with a function call leads to incorrect assumptions about who saves what.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, processor state includes more than general-purpose registers.

## Slide 14
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.6 ISA versus microarchitecture
SOURCE TOPIC
• The ISA specifies architectural behavior.
• The microarchitecture is the implementation: pipelines, execution units, caches, predictors, queues, and scheduling logic.
• Different processors can execute the same binary while exhibiting different latency, throughput, and energy behavior.
• An optimization based on a particular instruction cost may not transfer to another processor implementing the same ISA.
CHAPTER 12 | 14
Notes: SLIDE 14: 12.6 ISA versus microarchitecture
LECTURE NARRATION
The ISA specifies architectural behavior. The microarchitecture is the implementation: pipelines, execution units, caches, predictors, queues, and scheduling logic. Different processors can execute the same binary while exhibiting different latency, throughput, and energy behavior. An optimization based on a particular instruction cost may not transfer to another processor implementing the same ISA. The portable part of the reasoning is the algorithm and architectural semantics; the measured part belongs to a specific machine and workload. The Intel architecture manuals separate instruction behavior from implementation-oriented performance guidance. [ R3 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the ISA specifies architectural behavior.

## Slide 15
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
12.6 ISA versus microarchitecture — Deep Dive
ENGINEERING IMPLICATIONS
• An optimization based on a particular instruction cost may not transfer to another processor implementing the same ISA.
• The portable part of the reasoning is the algorithm and architectural semantics; the measured part belongs to a specific machine and workload.
• The Intel architecture manuals separate instruction behavior from implementation-oriented performance guidance. [ R3 ]
CHAPTER 12 | 15
Notes: SLIDE 15: 12.6 ISA versus microarchitecture — Deep Dive
LECTURE NARRATION
The ISA specifies architectural behavior. The microarchitecture is the implementation: pipelines, execution units, caches, predictors, queues, and scheduling logic. Different processors can execute the same binary while exhibiting different latency, throughput, and energy behavior. An optimization based on a particular instruction cost may not transfer to another processor implementing the same ISA. The portable part of the reasoning is the algorithm and architectural semantics; the measured part belongs to a specific machine and workload. The Intel architecture manuals separate instruction behavior from implementation-oriented performance guidance. [ R3 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the ISA specifies architectural behavior.

## Slide 16
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Tracing a tiny abstract machine
SOURCE TOPIC
• Use a deliberately simplified machine with one accumulator, a program counter, and four instructions: load immediate, add immediate, multiply immediate, and halt.
• This is a teaching model, not x86 assembly.
• Companion listing: ch12/machine.py
• The trace is (1,6) , (2,10) , and (3,30) .
CHAPTER 12 | 16
Notes: SLIDE 16: Worked example — Tracing a tiny abstract machine
LECTURE NARRATION
Use a deliberately simplified machine with one accumulator, a program counter, and four instructions: load immediate, add immediate, multiply immediate, and halt. This is a teaching model, not x86 assembly. Companion listing: ch12/machine.py The trace is (1,6) , (2,10) , and (3,30) . Each pair records the next instruction index and accumulator after one operation. The halt instruction leaves the final pair unchanged. The model makes control and data state explicit, but it intentionally omits fixed-width overflow, memory, interrupts, and timing. Now imagine an implementation that computes the addition and multiplication through several internal steps. As long as the architectural result at each required boundary is preserved, those internal steps need not resemble this simple interpreter. That is the distinction between an ISA-level explanation and an implementation-level explanation.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, use a deliberately simplified machine with one accumulator, a program counter, and four instructions: load immediate, add immediate, multiply immediate, and halt.

## Slide 17
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Tracing a tiny abstract machine — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• Companion listing: ch12/machine.py
• The trace is (1,6) , (2,10) , and (3,30) .
• Each pair records the next instruction index and accumulator after one operation.
• The halt instruction leaves the final pair unchanged.
CHAPTER 12 | 17
Notes: SLIDE 17: Worked example — Tracing a tiny abstract machine — Deep Dive
LECTURE NARRATION
Use a deliberately simplified machine with one accumulator, a program counter, and four instructions: load immediate, add immediate, multiply immediate, and halt. This is a teaching model, not x86 assembly. Companion listing: ch12/machine.py The trace is (1,6) , (2,10) , and (3,30) . Each pair records the next instruction index and accumulator after one operation. The halt instruction leaves the final pair unchanged. The model makes control and data state explicit, but it intentionally omits fixed-width overflow, memory, interrupts, and timing. Now imagine an implementation that computes the addition and multiplication through several internal steps. As long as the architectural result at each required boundary is preserved, those internal steps need not resemble this simple interpreter. That is the distinction between an ISA-level explanation and an implementation-level explanation.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, use a deliberately simplified machine with one accumulator, a program counter, and four instructions: load immediate, add immediate, multiply immediate, and halt.

## Slide 18
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Separating ISA from implementation
SOURCE TOPIC
• Two processors can both implement x86-64 and execute the same architectural instruction stream while using different pipelines, cache sizes, branch predictors, and execution...
• The ISA specifies programmer-visible behavior; the microarchitecture determines how a particular implementation achieves it.
• Performance differences therefore do not imply different source-level semantics.
CHAPTER 12 | 18
Notes: SLIDE 18: Worked example — Separating ISA from implementation
LECTURE NARRATION
Two processors can both implement x86-64 and execute the same architectural instruction stream while using different pipelines, cache sizes, branch predictors, and execution widths internally. The ISA specifies programmer-visible behavior; the microarchitecture determines how a particular implementation achieves it. Performance differences therefore do not imply different source-level semantics.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, two processors can both implement x86-64 and execute the same architectural instruction stream while using different pipelines, cache sizes, branch predictors, and execution widths internally.

## Slide 19
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Separating ISA from implementation — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• Two processors can both implement x86-64 and execute the same architectural instruction stream while using different pipelines, cache sizes, branch predictors, and...
• The ISA specifies programmer-visible behavior; the microarchitecture determines how a particular implementation achieves it.
• Performance differences therefore do not imply different source-level semantics.
CHAPTER 12 | 19
Notes: SLIDE 19: Worked example — Separating ISA from implementation — Deep Dive
LECTURE NARRATION
Two processors can both implement x86-64 and execute the same architectural instruction stream while using different pipelines, cache sizes, branch predictors, and execution widths internally. The ISA specifies programmer-visible behavior; the microarchitecture determines how a particular implementation achieves it. Performance differences therefore do not imply different source-level semantics.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, two processors can both implement x86-64 and execute the same architectural instruction stream while using different pipelines, cache sizes, branch predictors, and execution widths internally.

## Slide 20
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Updating architectural state
SOURCE TOPIC
• For an instruction conceptually equivalent to RAX = RAX + RBX , the visible result is a new RAX and updated condition flags according to the instruction definition.
• Internally the processor may rename registers and execute out of order, but retirement preserves the architectural effect as though the instruction completed in program order,...
CHAPTER 12 | 20
Notes: SLIDE 20: Worked example — Updating architectural state
LECTURE NARRATION
For an instruction conceptually equivalent to RAX = RAX + RBX , the visible result is a new RAX and updated condition flags according to the instruction definition. Internally the processor may rename registers and execute out of order, but retirement preserves the architectural effect as though the instruction completed in program order, subject to the machine’s defined memory model.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, for an instruction conceptually equivalent to RAX = RAX + RBX , the visible result is a new RAX and updated condition flags according to the instruction definition.

## Slide 21
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Updating architectural state — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• For an instruction conceptually equivalent to RAX = RAX + RBX , the visible result is a new RAX and updated condition flags according to the instruction definition.
• Internally the processor may rename registers and execute out of order, but retirement preserves the architectural effect as though the instruction completed in program...
CHAPTER 12 | 21
Notes: SLIDE 21: Worked example — Updating architectural state — Deep Dive
LECTURE NARRATION
For an instruction conceptually equivalent to RAX = RAX + RBX , the visible result is a new RAX and updated condition flags according to the instruction definition. Internally the processor may rename registers and execute out of order, but retirement preserves the architectural effect as though the instruction completed in program order, subject to the machine’s defined memory model.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, for an instruction conceptually equivalent to RAX = RAX + RBX , the visible result is a new RAX and updated condition flags according to the instruction definition.

## Slide 22
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Guided lab and review
SOURCE TOPIC
• Lab 12.
• Extend the model with a conditional branch and a bounded instruction-step limit.
• Use it to sum integers from one through five.
• Record the accumulator and program counter after every executed instruction.
CHAPTER 12 | 22
Notes: SLIDE 22: Guided lab and review
LECTURE NARRATION
Lab 12. Extend the model with a conditional branch and a bounded instruction-step limit. Use it to sum integers from one through five. Record the accumulator and program counter after every executed instruction. Review 1. Why can two processors run the same executable at different speeds? Review 2. Why is a function-call save convention smaller than the full processor state?
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, lab 12.

## Slide 23
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Guided lab and review — Deep Dive
LAB, REVIEW & ACCEPTANCE
• Review 1.
• Why can two processors run the same executable at different speeds?
• Review 2.
• Why is a function-call save convention smaller than the full processor state?
CHAPTER 12 | 23
Notes: SLIDE 23: Guided lab and review — Deep Dive
LECTURE NARRATION
Lab 12. Extend the model with a conditional branch and a bounded instruction-step limit. Use it to sum integers from one through five. Record the accumulator and program counter after every executed instruction. Review 1. Why can two processors run the same executable at different speeds? Review 2. Why is a function-call save convention smaller than the full processor state?
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, lab 12.

## Slide 24
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter Synthesis
KEY TAKEAWAYS
• The chapter's central subject is instruction set architecture.
• Correct reasoning requires explicit assumptions, bounds, ownership, and interface contracts.
• Observed behavior is evidence about a run; it is not automatically a language or system guarantee.
• Use the worked examples and lab to test whether the model transfers to new cases.
CHAPTER 12 | 24
Notes: SLIDE 24: Chapter Synthesis
LECTURE NARRATION
The chapter's central subject is instruction set architecture. Correct reasoning requires explicit assumptions, bounds, ownership, and interface contracts. Observed behavior is evidence about a run; it is not automatically a language or system guarantee. Use the worked examples and lab to test whether the model transfers to new cases.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the chapter's central subject is instruction set architecture.

## Slide 25
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Review and Transition
CHECK YOUR MODEL
• Explain one mechanism from the chapter without relying on vocabulary alone.
• Identify one failure mode and the violated contract or invariant.
• State what evidence would support your diagnosis and what it would not prove.
• Next: x86-64 Registers.
CHAPTER 12 | 25
Notes: SLIDE 25: Review and Transition
LECTURE NARRATION
Explain one mechanism from the chapter without relying on vocabulary alone. Identify one failure mode and the violated contract or invariant. State what evidence would support your diagnosis and what it would not prove. Next: x86-64 Registers.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, explain one mechanism from the chapter without relying on vocabulary alone.