## Slide 1
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter 54 — Measuring Performance
GRADUATE LECTURE
• Performance engineering begins by defining the work and the measurement boundary.
• A number is meaningful only when it identifies what completed, under which conditions, and how the observation was made.
• Correctness checks belong in the experiment: a program that skips work can appear extraordinarily fast.
• This chapter distinguishes measured observations , analytical models , and illustrative assumptions .
CHAPTER 54 | 1
Notes: SLIDE 1: Chapter 54 — Measuring Performance
LECTURE NARRATION
Performance engineering begins by defining the work and the measurement boundary. A number is meaningful only when it identifies what completed, under which conditions, and how the observation was made. Correctness checks belong in the experiment: a program that skips work can appear extraordinarily fast. This chapter distinguishes measured observations , analytical models , and illustrative assumptions . The companion benchmark reports local timings when run, but the book does not convert one container run into a universal hardware claim. Reproduce measurements on the machine and workload that matter. [ R30 , R42 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, performance engineering begins by defining the work and the measurement boundary.

## Slide 2
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
What This Chapter Builds
LEARNING OBJECTIVES
• Explain the mechanisms and contracts in Measuring Performance.
• Trace the chapter's important state, representation, and resource transitions.
• Identify failure modes, assumptions, and evidence required for correctness.
• Apply the chapter model to the worked examples and guided lab.
CHAPTER 54 | 2
Notes: SLIDE 2: What This Chapter Builds
LECTURE NARRATION
Performance engineering begins by defining the work and the measurement boundary. A number is meaningful only when it identifies what completed, under which conditions, and how the observation was made. Correctness checks belong in the experiment: a program that skips work can appear extraordinarily fast. This chapter distinguishes measured observations , analytical models , and illustrative assumptions . The companion benchmark reports local timings when run, but the book does not convert one container run into a universal hardware claim. Reproduce measurements on the machine and workload that matter. [ R30 , R42 ]
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, performance engineering begins by defining the work and the measurement boundary.

## Slide 3
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter Roadmap
SOURCE-ALIGNED COVERAGE
• 54.1 Latency
• 54.2 Throughput
• 54.3 CPU time
• 54.4 Wall-clock time
• ...plus 7 additional source topics
CHAPTER 54 | 3
Notes: SLIDE 3: Chapter Roadmap
LECTURE NARRATION
54.1 Latency 54.2 Throughput 54.3 CPU time 54.4 Wall-clock time ...plus 7 additional source topics
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, 54.1 Latency 54.2 Throughput 54.3 CPU time 54.4 Wall-clock time ...plus 7 additional source topics

## Slide 4
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.1 Latency
SOURCE TOPIC
• Latency measures elapsed time from a defined start event to a defined completion event.
• For a request, the boundary might include queueing, parsing, computation, and response delivery.
• For a kernel, it might include only the computation after inputs are prepared.
• Report a distribution when requests vary.
CHAPTER 54 | 4
Notes: SLIDE 4: 54.1 Latency
LECTURE NARRATION
Latency measures elapsed time from a defined start event to a defined completion event. For a request, the boundary might include queueing, parsing, computation, and response delivery. For a kernel, it might include only the computation after inputs are prepared. Report a distribution when requests vary. A mean can hide a long tail, and a percentile requires enough samples and a clearly defined population. Do not compare one system’s median service time with another system’s end-to-end 99th percentile as though they were the same metric.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, latency measures elapsed time from a defined start event to a defined completion event.

## Slide 5
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.1 Latency — Deep Dive
ENGINEERING IMPLICATIONS
• Report a distribution when requests vary.
• A mean can hide a long tail, and a percentile requires enough samples and a clearly defined population.
• Do not compare one system’s median service time with another system’s end-to-end 99th percentile as though they were the same metric.
CHAPTER 54 | 5
Notes: SLIDE 5: 54.1 Latency — Deep Dive
LECTURE NARRATION
Latency measures elapsed time from a defined start event to a defined completion event. For a request, the boundary might include queueing, parsing, computation, and response delivery. For a kernel, it might include only the computation after inputs are prepared. Report a distribution when requests vary. A mean can hide a long tail, and a percentile requires enough samples and a clearly defined population. Do not compare one system’s median service time with another system’s end-to-end 99th percentile as though they were the same metric.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, latency measures elapsed time from a defined start event to a defined completion event.

## Slide 6
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.2 Throughput
SOURCE TOPIC
• Throughput measures completed useful work per unit time.
• It can be expressed as records, requests, or bytes per second.
• Define whether failed requests, retries, warmup work, and partial completions count.
• Throughput and latency interact through queueing.
CHAPTER 54 | 6
Notes: SLIDE 6: 54.2 Throughput
LECTURE NARRATION
Throughput measures completed useful work per unit time. It can be expressed as records, requests, or bytes per second. Define whether failed requests, retries, warmup work, and partial completions count. Throughput and latency interact through queueing. A system can increase completed work by admitting more concurrent requests while making each request wait longer. Evaluate the service objective rather than maximizing a single number without constraints.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, throughput measures completed useful work per unit time.

## Slide 7
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.2 Throughput — Deep Dive
ENGINEERING IMPLICATIONS
• Throughput and latency interact through queueing.
• A system can increase completed work by admitting more concurrent requests while making each request wait longer.
• Evaluate the service objective rather than maximizing a single number without constraints.
CHAPTER 54 | 7
Notes: SLIDE 7: 54.2 Throughput — Deep Dive
LECTURE NARRATION
Throughput measures completed useful work per unit time. It can be expressed as records, requests, or bytes per second. Define whether failed requests, retries, warmup work, and partial completions count. Throughput and latency interact through queueing. A system can increase completed work by admitting more concurrent requests while making each request wait longer. Evaluate the service objective rather than maximizing a single number without constraints.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, throughput measures completed useful work per unit time.

## Slide 8
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.3 CPU time
SOURCE TOPIC
• CPU time measures processor execution charged to a process or thread under the operating system’s accounting rules.
• It excludes many periods spent blocked or not scheduled.
• A multithreaded process can accumulate more total CPU time than elapsed wall time when several threads execute concurrently.
• CPU time helps distinguish computation from waiting, but it is not a complete explanation.
CHAPTER 54 | 8
Notes: SLIDE 8: 54.3 CPU time
LECTURE NARRATION
CPU time measures processor execution charged to a process or thread under the operating system’s accounting rules. It excludes many periods spent blocked or not scheduled. A multithreaded process can accumulate more total CPU time than elapsed wall time when several threads execute concurrently. CPU time helps distinguish computation from waiting, but it is not a complete explanation. Kernel activity, helper processes, and accounting boundaries may contribute differently. State whether the measurement covers one thread, the whole process, or a larger job.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, cPU time measures processor execution charged to a process or thread under the operating system’s accounting rules.

## Slide 9
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.3 CPU time — Deep Dive
ENGINEERING IMPLICATIONS
• CPU time helps distinguish computation from waiting, but it is not a complete explanation.
• Kernel activity, helper processes, and accounting boundaries may contribute differently.
• State whether the measurement covers one thread, the whole process, or a larger job.
CHAPTER 54 | 9
Notes: SLIDE 9: 54.3 CPU time — Deep Dive
LECTURE NARRATION
CPU time measures processor execution charged to a process or thread under the operating system’s accounting rules. It excludes many periods spent blocked or not scheduled. A multithreaded process can accumulate more total CPU time than elapsed wall time when several threads execute concurrently. CPU time helps distinguish computation from waiting, but it is not a complete explanation. Kernel activity, helper processes, and accounting boundaries may contribute differently. State whether the measurement covers one thread, the whole process, or a larger job.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, cPU time measures processor execution charged to a process or thread under the operating system’s accounting rules.

## Slide 10
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.4 Wall-clock time
SOURCE TOPIC
• Wall-clock elapsed time includes waiting, scheduling delays, and other activity between the chosen start and end.
• For duration measurements, use a monotonic clock such as std::chrono::steady_clock rather than a civil-time clock that can be adjusted.
• Clock resolution and call overhead matter for very small operations.
• Batch enough work to make the measured interval meaningful, while ensuring that the batch still represents the workload and does not change cache behavior beyond the intended...
CHAPTER 54 | 10
Notes: SLIDE 10: 54.4 Wall-clock time
LECTURE NARRATION
Wall-clock elapsed time includes waiting, scheduling delays, and other activity between the chosen start and end. For duration measurements, use a monotonic clock such as std::chrono::steady_clock rather than a civil-time clock that can be adjusted. Clock resolution and call overhead matter for very small operations. Batch enough work to make the measured interval meaningful, while ensuring that the batch still represents the workload and does not change cache behavior beyond the intended experiment.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, wall-clock elapsed time includes waiting, scheduling delays, and other activity between the chosen start and end.

## Slide 11
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.4 Wall-clock time — Deep Dive
ENGINEERING IMPLICATIONS
• Clock resolution and call overhead matter for very small operations.
• Batch enough work to make the measured interval meaningful, while ensuring that the batch still represents the workload and does not change cache behavior beyond the...
CHAPTER 54 | 11
Notes: SLIDE 11: 54.4 Wall-clock time — Deep Dive
LECTURE NARRATION
Wall-clock elapsed time includes waiting, scheduling delays, and other activity between the chosen start and end. For duration measurements, use a monotonic clock such as std::chrono::steady_clock rather than a civil-time clock that can be adjusted. Clock resolution and call overhead matter for very small operations. Batch enough work to make the measured interval meaningful, while ensuring that the batch still represents the workload and does not change cache behavior beyond the intended experiment.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, wall-clock elapsed time includes waiting, scheduling delays, and other activity between the chosen start and end.

## Slide 12
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.5 Utilization
SOURCE TOPIC
• Utilization describes the fraction of a resource’s capacity in use under a stated definition.
• CPU utilization, memory bandwidth utilization, and device busy time are different metrics.
• High CPU utilization does not prove that useful work is progressing efficiently; a spin loop can consume an entire core.
• Low utilization does not automatically mean spare end-to-end capacity.
CHAPTER 54 | 12
Notes: SLIDE 12: 54.5 Utilization
LECTURE NARRATION
Utilization describes the fraction of a resource’s capacity in use under a stated definition. CPU utilization, memory bandwidth utilization, and device busy time are different metrics. High CPU utilization does not prove that useful work is progressing efficiently; a spin loop can consume an entire core. Low utilization does not automatically mean spare end-to-end capacity. The bottleneck may be a serialized dependency, a lock, a downstream service, or a limit in another resource. Identify the constrained stage before adding more work.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, utilization describes the fraction of a resource’s capacity in use under a stated definition.

## Slide 13
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.5 Utilization — Deep Dive
ENGINEERING IMPLICATIONS
• Low utilization does not automatically mean spare end-to-end capacity.
• The bottleneck may be a serialized dependency, a lock, a downstream service, or a limit in another resource.
• Identify the constrained stage before adding more work.
CHAPTER 54 | 13
Notes: SLIDE 13: 54.5 Utilization — Deep Dive
LECTURE NARRATION
Utilization describes the fraction of a resource’s capacity in use under a stated definition. CPU utilization, memory bandwidth utilization, and device busy time are different metrics. High CPU utilization does not prove that useful work is progressing efficiently; a spin loop can consume an entire core. Low utilization does not automatically mean spare end-to-end capacity. The bottleneck may be a serialized dependency, a lock, a downstream service, or a limit in another resource. Identify the constrained stage before adding more work.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, utilization describes the fraction of a resource’s capacity in use under a stated definition.

## Slide 14
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.6 Benchmarking
SOURCE TOPIC
• A benchmark should state input size and distribution, build configuration, machine context, warmup policy, repetition count, and correctness criteria.
• Keep setup outside the timed region when the goal excludes setup, and include it when evaluating end-to-end behavior.
• Preserve observable results so the compiler cannot legally discard the intended work as unused.
• Inspect generated code when a result seems implausible.
CHAPTER 54 | 14
Notes: SLIDE 14: 54.6 Benchmarking
LECTURE NARRATION
A benchmark should state input size and distribution, build configuration, machine context, warmup policy, repetition count, and correctness criteria. Keep setup outside the timed region when the goal excludes setup, and include it when evaluating end-to-end behavior. Preserve observable results so the compiler cannot legally discard the intended work as unused. Inspect generated code when a result seems implausible. Avoid volatile as a blanket benchmarking technique because it can change the workload being measured rather than merely prevent elimination.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a benchmark should state input size and distribution, build configuration, machine context, warmup policy, repetition count, and correctness criteria.

## Slide 15
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.6 Benchmarking — Deep Dive
ENGINEERING IMPLICATIONS
• Preserve observable results so the compiler cannot legally discard the intended work as unused.
• Inspect generated code when a result seems implausible.
• Avoid volatile as a blanket benchmarking technique because it can change the workload being measured rather than merely prevent elimination.
CHAPTER 54 | 15
Notes: SLIDE 15: 54.6 Benchmarking — Deep Dive
LECTURE NARRATION
A benchmark should state input size and distribution, build configuration, machine context, warmup policy, repetition count, and correctness criteria. Keep setup outside the timed region when the goal excludes setup, and include it when evaluating end-to-end behavior. Preserve observable results so the compiler cannot legally discard the intended work as unused. Inspect generated code when a result seems implausible. Avoid volatile as a blanket benchmarking technique because it can change the workload being measured rather than merely prevent elimination.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a benchmark should state input size and distribution, build configuration, machine context, warmup policy, repetition count, and correctness criteria.

## Slide 16
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.7 Measurement error
SOURCE TOPIC
• Measurements vary because of scheduling, frequency changes, contention, cache state, page faults, thermal behavior, and instrumentation overhead.
• Repeated samples reveal variation but do not automatically remove bias.
• Change one factor at a time where practical and alternate comparison order to reduce drift effects.
• Report uncertainty honestly.
CHAPTER 54 | 16
Notes: SLIDE 16: 54.7 Measurement error
LECTURE NARRATION
Measurements vary because of scheduling, frequency changes, contention, cache state, page faults, thermal behavior, and instrumentation overhead. Repeated samples reveal variation but do not automatically remove bias. Change one factor at a time where practical and alternate comparison order to reduce drift effects. Report uncertainty honestly. A difference smaller than the experiment’s noise is not strong evidence of improvement, and a statistically clear difference may still be too small to matter operationally.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, measurements vary because of scheduling, frequency changes, contention, cache state, page faults, thermal behavior, and instrumentation overhead.

## Slide 17
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
54.7 Measurement error — Deep Dive
ENGINEERING IMPLICATIONS
• Change one factor at a time where practical and alternate comparison order to reduce drift effects.
• Report uncertainty honestly.
• A difference smaller than the experiment’s noise is not strong evidence of improvement, and a statistically clear difference may still be too small to matter operationally.
CHAPTER 54 | 17
Notes: SLIDE 17: 54.7 Measurement error — Deep Dive
LECTURE NARRATION
Measurements vary because of scheduling, frequency changes, contention, cache state, page faults, thermal behavior, and instrumentation overhead. Repeated samples reveal variation but do not automatically remove bias. Change one factor at a time where practical and alternate comparison order to reduce drift effects. Report uncertainty honestly. A difference smaller than the experiment’s noise is not strong evidence of improvement, and a statistically clear difference may still be too small to matter operationally.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, measurements vary because of scheduling, frequency changes, contention, cache state, page faults, thermal behavior, and instrumentation overhead.

## Slide 18
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — A checksum-protected timing boundary
SOURCE TOPIC
• This program constructs a bounded runtime-sized vector, times one summation, and verifies the sum against an independent formula.
• Setup and verification are outside the timed interval.
• The output timing is an observation on the machine where it is run, not a fixed expected value.
• Companion listing: ch54/benchmark.cpp
CHAPTER 54 | 18
Notes: SLIDE 18: Worked example — A checksum-protected timing boundary
LECTURE NARRATION
This program constructs a bounded runtime-sized vector, times one summation, and verifies the sum against an independent formula. Setup and verification are outside the timed interval. The output timing is an observation on the machine where it is run, not a fixed expected value. Companion listing: ch54/benchmark.cpp For count 1000, there are three complete groups of values 0 through 250 and a remainder of 247 values, 0 through 246. The expected sum is 3 × 31375 + 247 × 246/2 = 124506 . The elapsed nanoseconds vary. A zero or very small reported duration for a tiny input can reflect clock granularity or overhead dominance rather than infinite throughput. The program is a measurement-mechanics example, not a complete microbenchmark framework. Repeat separate runs, record build flags, inspect the loop, and compare like conditions before interpreting a performance difference. Allocation failure is reported by the C++ runtime unless a surrounding application adds a more specific recovery policy.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, this program constructs a bounded runtime-sized vector, times one summation, and verifies the sum against an independent formula.

## Slide 19
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — A checksum-protected timing boundary — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• Companion listing: ch54/benchmark.cpp
• For count 1000, there are three complete groups of values 0 through 250 and a remainder of 247 values, 0 through 246.
• The expected sum is 3 × 31375 + 247 × 246/2 = 124506 .
• The elapsed nanoseconds vary.
CHAPTER 54 | 19
Notes: SLIDE 19: Worked example — A checksum-protected timing boundary — Deep Dive
LECTURE NARRATION
This program constructs a bounded runtime-sized vector, times one summation, and verifies the sum against an independent formula. Setup and verification are outside the timed interval. The output timing is an observation on the machine where it is run, not a fixed expected value. Companion listing: ch54/benchmark.cpp For count 1000, there are three complete groups of values 0 through 250 and a remainder of 247 values, 0 through 246. The expected sum is 3 × 31375 + 247 × 246/2 = 124506 . The elapsed nanoseconds vary. A zero or very small reported duration for a tiny input can reflect clock granularity or overhead dominance rather than infinite throughput. The program is a measurement-mechanics example, not a complete microbenchmark framework. Repeat separate runs, record build flags, inspect the loop, and compare like conditions before interpreting a performance difference. Allocation failure is reported by the C++ runtime unless a surrounding application adds a more specific recovery policy.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, this program constructs a bounded runtime-sized vector, times one summation, and verifies the sum against an independent formula.

## Slide 20
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Throughput and latency
SOURCE TOPIC
• If a service completes 12,000 requests in 60 seconds, average throughput is 200 requests/s.
• That fact does not reveal individual latency: one request may complete in 2 ms while another waits 500 ms.
• Report throughput and latency distributions separately because batching and queueing can improve one while harming the other.
CHAPTER 54 | 20
Notes: SLIDE 20: Worked example — Throughput and latency
LECTURE NARRATION
If a service completes 12,000 requests in 60 seconds, average throughput is 200 requests/s. That fact does not reveal individual latency: one request may complete in 2 ms while another waits 500 ms. Report throughput and latency distributions separately because batching and queueing can improve one while harming the other.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, if a service completes 12,000 requests in 60 seconds, average throughput is 200 requests/s.

## Slide 21
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — Throughput and latency — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• If a service completes 12,000 requests in 60 seconds, average throughput is 200 requests/s.
• That fact does not reveal individual latency: one request may complete in 2 ms while another waits 500 ms.
• Report throughput and latency distributions separately because batching and queueing can improve one while harming the other.
CHAPTER 54 | 21
Notes: SLIDE 21: Worked example — Throughput and latency — Deep Dive
LECTURE NARRATION
If a service completes 12,000 requests in 60 seconds, average throughput is 200 requests/s. That fact does not reveal individual latency: one request may complete in 2 ms while another waits 500 ms. Report throughput and latency distributions separately because batching and queueing can improve one while harming the other.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, if a service completes 12,000 requests in 60 seconds, average throughput is 200 requests/s.

## Slide 22
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — CPU time versus wall time
SOURCE TOPIC
• A task reports 2.0 s wall-clock time but only 0.6 s CPU time.
• The remaining elapsed time may include waiting for I/O, scheduling delays, or sleeps.
• Optimizing arithmetic cannot remove time spent blocked on a slow dependency unless the design changes that dependency or overlaps it with other work.
CHAPTER 54 | 22
Notes: SLIDE 22: Worked example — CPU time versus wall time
LECTURE NARRATION
A task reports 2.0 s wall-clock time but only 0.6 s CPU time. The remaining elapsed time may include waiting for I/O, scheduling delays, or sleeps. Optimizing arithmetic cannot remove time spent blocked on a slow dependency unless the design changes that dependency or overlaps it with other work.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a task reports 2.0 s wall-clock time but only 0.6 s CPU time.

## Slide 23
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Worked example — CPU time versus wall time — Deep Dive
WORKED EXAMPLE & INTERPRETATION
• A task reports 2.0 s wall-clock time but only 0.6 s CPU time.
• The remaining elapsed time may include waiting for I/O, scheduling delays, or sleeps.
• Optimizing arithmetic cannot remove time spent blocked on a slow dependency unless the design changes that dependency or overlaps it with other work.
CHAPTER 54 | 23
Notes: SLIDE 23: Worked example — CPU time versus wall time — Deep Dive
LECTURE NARRATION
A task reports 2.0 s wall-clock time but only 0.6 s CPU time. The remaining elapsed time may include waiting for I/O, scheduling delays, or sleeps. Optimizing arithmetic cannot remove time spent blocked on a slow dependency unless the design changes that dependency or overlaps it with other work.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, a task reports 2.0 s wall-clock time but only 0.6 s CPU time.

## Slide 24
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Guided lab and review
SOURCE TOPIC
• Lab 54.
• Run several input sizes and record count, verified sum, elapsed time, compiler version, flags, and repetition number.
• Keep raw samples rather than reporting only the fastest.
• Explain whether the benchmark includes allocation, initialization, and output.
CHAPTER 54 | 24
Notes: SLIDE 24: Guided lab and review
LECTURE NARRATION
Lab 54. Run several input sizes and record count, verified sum, elapsed time, compiler version, flags, and repetition number. Keep raw samples rather than reporting only the fastest. Explain whether the benchmark includes allocation, initialization, and output. Review 1. Why use a monotonic clock? Review 2. Can total CPU time exceed wall time for a multithreaded program?
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, lab 54.

## Slide 25
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Guided lab and review — Deep Dive
LAB, REVIEW & ACCEPTANCE
• Review 1.
• Why use a monotonic clock?
• Review 2.
• Can total CPU time exceed wall time for a multithreaded program?
CHAPTER 54 | 25
Notes: SLIDE 25: Guided lab and review — Deep Dive
LECTURE NARRATION
Lab 54. Run several input sizes and record count, verified sum, elapsed time, compiler version, flags, and repetition number. Keep raw samples rather than reporting only the fastest. Explain whether the benchmark includes allocation, initialization, and output. Review 1. Why use a monotonic clock? Review 2. Can total CPU time exceed wall time for a multithreaded program?
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, lab 54.

## Slide 26
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Chapter Synthesis
KEY TAKEAWAYS
• The chapter's central subject is measuring performance.
• Correct reasoning requires explicit assumptions, bounds, ownership, and interface contracts.
• Observed behavior is evidence about a run; it is not automatically a language or system guarantee.
• Use the worked examples and lab to test whether the model transfers to new cases.
CHAPTER 54 | 26
Notes: SLIDE 26: Chapter Synthesis
LECTURE NARRATION
The chapter's central subject is measuring performance. Correct reasoning requires explicit assumptions, bounds, ownership, and interface contracts. Observed behavior is evidence about a run; it is not automatically a language or system guarantee. Use the worked examples and lab to test whether the model transfers to new cases.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, the chapter's central subject is measuring performance.

## Slide 27
SYSTEMS PROGRAMMING AND MACHINE ORGANIZATION · CHARLES DORNER
Review and Transition
CHECK YOUR MODEL
• Explain one mechanism from the chapter without relying on vocabulary alone.
• Identify one failure mode and the violated contract or invariant.
• State what evidence would support your diagnosis and what it would not prove.
• Next: Program Optimization.
CHAPTER 54 | 27
Notes: SLIDE 27: Review and Transition
LECTURE NARRATION
Explain one mechanism from the chapter without relying on vocabulary alone. Identify one failure mode and the violated contract or invariant. State what evidence would support your diagnosis and what it would not prove. Next: Program Optimization.
At graduate level, do not treat this as a term to memorize. Identify the contract being described, the state or representation it constrains, and the assumptions that must remain true. When this topic appears in real systems code, separate what the language guarantees from what a compiler, operating system, ABI, ISA, or particular machine happens to do. Then identify the evidence you would inspect to test the claim without overgeneralizing from a single successful run.
SIXTH-GRADE EXPLANATION
In simpler terms, explain one mechanism from the chapter without relying on vocabulary alone.